## Slide 1: Edit the one that’s on OneDrive
Not this one

## Slide 2: Introduction
Image and video analysis software must use computer vision techniques to identify times shown on analog clocks
Modern implementations of image analysis use complicated computer learning/artificial-intelligence techniques
Classical computer vision techniques can be used to simplify process
10:10
Edit the one that’s on OneDrive

## Slide 3: Theory
Identify and Isolate
Identify and isolate analog clocks from input image
Pre-Processing
Blur pertinent regions to remove noise/unnecessary clock features
Edge Detection
Perform edge detection
Line Detection
Perform line detection of edge map, compare line lengths to determine minute/hour hand
Classification
Determine hour and minute from gradient direction/detected line angles
Edit the one that’s on OneDrive

## Slide 4: Pre-Processing
Provided image matrix of interest region, some clock faces have branding/writing which must be ignored
Second hand on some clocks may be same length as minute hand; only distinguishable by watching clock in real-time. Try to remove second hand using strong Gaussian blur.
Gaussian smoothing can remove unnecessary features, making edge and line detection easier
Edit the one that’s on OneDrive

## Slide 5: Edge and Line Detection
Provided binary input image, edges must be detected so that line section can take place.
Canny Edge Detector used with threshold = 0.5
Hough Transform performed on edge map from Canny Edge Detector
Edit the one that’s on OneDrive

## Slide 6: Hough Transform
Hough Transform will identify lines from hour/minute hands, as well as other not-important lines
Hough parameters needed to be hand-tuned
  Number of peaks = 5
  Minimum Line Length = 100
  Hough Threshold = 1% of H max
Edit the one that’s on OneDrive

## Slide 7
Edit the one that’s on OneDrive